Transformed E&M I homework

Electric Displacement

(Griffiths Chapter 4)

Electric displacement

Question   Field patterns from bound charges

Let's go back to the "solid" teflon rod (radius a), but let's change the polarization once again - now assume it is uniform and parallel to the z-axis, i.e. P . This time, let's also keep it finite, and consider realistic "end effects"

a) Sketch the electric field lines, inside and outside, in two different limits: First, when the cylinder is very LONG compared to its diameter, and second, when it is very SHORT compared to its diameter. Explain in words and formulas your physical reasoning behind the sketches.

b) In both of the above two limiting cases, sketch (and explain in words) P everywhere in space, and also D everywhere (inside and outside the rods)

c)  In both of the above limits, explain how Griffiths' "boundary condition" (page 178) Eq 4.26 and 4.28 work out near the top end of the rod.

Also (just briefly, very qualitatively, e.g. simply in terms of signs or directions of these fields) explain how boundary conditions 4.27 and 4.29 makes sense/agree with your sketches in part b. (Here, you only need to really consider the outer edge of the middle of the cylinder at z=0 i.e. at  (s=a, z=0) if the rod runs from z=-L to z=+L)

Such an object is referred to as a "bar electret", it is an electrical analogue of a permanent bar magnet. Do you see why, from your sketches? Griffiths points out that this is quite unusual, most materials cannot maintain such a permanent electric polarization in the absence of an external field, although he claims they do exist. But if you did have one, it would attract charged ions from the air which would negate the interesting fields you found above.

Assigned in SP08 (average score: a) 4.24, b) 7.09, c) 4.90)

Instructor notes: This is a hard problem for students and many leave it blank.  Some students struggle with how to find the E field or D field.  This was especially troublesome for the long thin rod, where they hadn't realized they could estimate E in various "limiting regions" and thence get D.  Many think that E field is uniform inside the rod in the limiting case of a long rod.

Question   D and E of dielectric slab at an angle to external E

GAUSS’ LAW; CALCULATION (U. Nauenberg; solutions available)

Consider an uncharged dielectric slab of material with dielectric constant epsilon, so placed that the normal to the slab is at an angle of 30 degrees to the direction

of an incident electric field “E”. Obtain mathematical expressions describing

the magnitude and direction of the “E” and “D” fields, and of the dipole

moment “P” inside the dielectric.

Question   Varying dielectric constant

GAUSS’ LAW; CALCULATION (U. Nauenberg, solutions available)

A dielectric material separates two conducting plates. The area of the

plates is “A” and a charge “+Q” is placed on one plate and “-Q” on the

other. The separation between the plates is “t”. Assume that the area of the

plates is much large than the separation so that you can neglect edge effects.

The dielectric constant varies linearly between the plates as follows:

(a)Find expressions for the Displacement field “D” and the dipole moment

“P” between the plates.

(b)Find expressions for the “E field” everywhere, between the plates and on

the outside of the plates.

(c)Obtain an expression for the potential difference between the plates.

Question   Dielectric sphere

GAUSS’ LAW; CALCULATION (U. Nauenberg, solutions available)

A sphere of radius “R” is made up of a dielectric material with dielectric

constant eispolon̨ and contains a uniform free charge density per unit volume ρf .

Show that the potential at the center is given by:

Question   Concentric spherical shells with dielectric liquid

BOUNDARY CONDITIONS; CALCULATION (U. Nauenberg, solutions available)

Consider two concentric conducting spherical shells of radii a and b as

shown in the figure. The space between them is half filled with a liquid

having a dielectric constant “ǫ”. A total charge of “+Q” is placed in the

inner shell and “-Q” in the outer shell.

This is a beautifull example of the power of the uniqueness theorem. Be

careful to satisfy the boundary conditions everywhere, including the bound-

ary between the dielectric and the air in between the spherical shells. If you

think a bit about satisfying the boundary conditions you will notice that the

solution for the “E” field is very simple.

a)Find the magnitude and direction of the fields E, D, P everywhere; namely

for r > b, a < r < b, and r < a.

b)Determine expressions for the free surface charge on each conducting shell

everywhere (namely, on the dielectric side, and the air side).

c)Determine expressions for the bound charge at r = a and r = b.

d)Determine the potential everywhere.

Question   Charge density and E field of charged dielectric cylindrical shell

GAUSS’ LAW, ESTIMATIONS (OSU Paradigms, Vector Fields HW9)

We have solutions to this in OSU folder