## Slide 1: CURRENTS, OHM’S LAW

## Slide 2: For everyday currents in home electronics and wires, which answer is the order of magnitude of the average velocity of the electrons along the wire?
km/s
m/s
mm/s
μm/s
nm/s
7.1a
Notes: CORRECT ANSWER: C
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 14, Lecture 40)
STUDENT RESPONSES: 0% 19% [[33%]] 49% 0% (FALL 2008)
INSTRUCTOR NOTES:
WRITTEN BY: Ed Kinney CU-Boulder)

## Slide 3: For everyday currents in home electronics and wires, which answer is the order of magnitude of the instantaneous speed of the electrons in the wire?
km/s
m/s
mm/s
μm/s
nm/s
7.1b
Notes: CORRECT ANSWER: A
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 14, Lecture 40)
STUDENT RESPONSES: [[77%]] 23% 0% 0% 0% (FALL 2008)
INSTRUCTOR NOTES:
WRITTEN BY: Ed Kinney CU-Boulder)

## Slide 4: An electric current I flows along a copper wire (low resistivity) into a resistor made of carbon (high resistivity) then back into another copper wire. In which material is the electric field largest?
In the copper wire
In the carbon resistor
It’s the same in both copper and carbon
It depends on the sizes of the copper and carbon
I
7.2
Notes: CORRECT ANSWER: D
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 14, Lecture 40 and Week 14, Lecture 41)
STUDENT RESPONSES: 14% 34% 5% [[48%]] 0% (FALL 2008: Week 14, Lecture 40)
0% 14% 0% [[81%]] 6% (FALL 2008: Week 14, Lecture 41)
INSTRUCTOR NOTES:
WRITTEN BY: Ed Kinney CU-Boulder)

## Slide 5: An steady electric current I flows around a circuit containing a battery of voltage V and a resistor R. Which of the following statements about is true?
It is zero around the circuit because it’s an electrostatic field
It is non-zero around the circuit because it’s not an electrostatic field
It is zero around the circuit because of the electric field is not time dependent
It is non-zero around the circuit because there is no electric field in the battery, only in the rest of the circuit
None of the above
7.3
Notes: CORRECT ANSWER: E
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 14, Lecture 41)
STUDENT RESPONSES: 8% 54% 30% 0% [[8%]] (FALL 2008)
INSTRUCTOR NOTES:
WRITTEN BY: Ed Kinney CU-Boulder)

## Slide 6: Charge Conservation
Which of the following is a statement of charge conservation?
A)
B)
C)
D)
E) Not sure/can't remember
5.10
Notes: 6
CORRECT ANSWER: D
USED IN: Spring 2008 (Pollock)
LECTURE NUMBER: 42
STUDENT RESPONSES: 0% 25% 25% [[50%]] 0%
INSTRUCTOR NOTES: Had given this L30 Start of class. 94% correct. (Right after spring break). Repeated this last lecture , now it's only 50% correct! (With B and D splitting the rest).This is slippery, apparently. "Units" ruled the day, but I reviewed what the equation means, and how to interpret it. (Didn't talk/remind of divergence theorem explicitly, but should have!) One student asked about B, she wanted to know how you would interpret the right side - nice question! I let other students answer ("current through") . -SJP
WRITTEN BY: Steven Pollock (CU-Boulder)

## Slide 7: MOTIONAL EMF

## Slide 8: One end of rectangular metal loop enters a region of constant uniform magnetic field B with speed v, as shown. In which direction does the current flow?
CW
CCW
Depends on the length of the sides
Depends on the resistivity of the metal
B
B
v
L
7.4
Notes: CORRECT ANSWER: A
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 14, Lecture 41)
STUDENT RESPONSES: [[97%]] 3% 0% 0% 0% (FALL 2008)
INSTRUCTOR NOTES:
WRITTEN BY: Ed Kinney CU-Boulder)

## Slide 9: One end of rectangular metal loop enters a region of constant uniform magnetic field B, with constant speed v, as shown. What direction is the net force on the loop?
Up the “screen” 
Down the “screen” 
To the right 
To the left 
The net force is zero
B
B
v
L
7.5
Notes: CORRECT ANSWER: D
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 15, Lecture 43)
STUDENT RESPONSES: 0% 49% 7% [[32%]] 12% (FALL 2008)
INSTRUCTOR NOTES:
WRITTEN BY: Ed Kinney CU-Boulder)

## Slide 10: One end of rectangular metal loop enters a region of constant uniform magnetic field B, with constant speed v, as shown. What is the flux through the loop at the instant shown?
LwB
-LwB
LxB
-LxB
0
B
B
v
L
w
x
7.6
Notes: CORRECT ANSWER: D
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 15, Lecture 43)
STUDENT RESPONSES: 0% 0% 12% [[88%]] 0% (FALL 2008)
INSTRUCTOR NOTES: Flux rule for motional emf
WRITTEN BY: Ed Kinney CU-Boulder)

## Slide 11: One end of stationary rectangular metal loop is in a region of uniform magnetic field B, which has magnitude B increasing with time as B=B0+kt. What is the emf around the loop?
Lxk
-Lxk
LxB0
-LxB0
0
B
B
L
w
x
7.7
Notes: CORRECT ANSWER: A
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 15, Lecture 43)
STUDENT RESPONSES: [[84%]] 9% 2% 5% 0% (FALL 2008)
INSTRUCTOR NOTES: Flux rule for induced emf
WRITTEN BY: Ed Kinney (CU-Boulder)

## Slide 12: One end of stationary rectangular metal loop is in a region of uniform magnetic field B, which has magnitude B increasing with time as B=B0+kt. What is the direction of the field Bind created by the induced current in the loop, in the plane region inside the loop?
Into the screen
Out of the screen
To the left
To the right
Not enough information
B
B
L
w
x
7.8
Notes: CORRECT ANSWER: A
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 15, Lecture 43)
STUDENT RESPONSES: [[100%]] 0% 0% 0% 0% (FALL 2008)
INSTRUCTOR NOTES: Flux rule for induced emf
WRITTEN BY: Ed Kinney (CU-Boulder)

## Slide 13: One end of stationary rectangular metal loop is in a region of uniform magnetic field B, which has magnitude B decreasing with time as B=B0-kt. What is the direction of the field Bind created by the induced current in the loop, in the plane region inside the loop?
Into the screen
Out of the screen
To the left
To the right
Not enough information
B
B
L
w
x
7.9
Notes: CORRECT ANSWER: B
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 15, Lecture 43)
STUDENT RESPONSES: 5% [[95%]] 0% 0% 0% (FALL 2008)
INSTRUCTOR NOTES: Flux rule for induced emf
WRITTEN BY: Ed Kinney (CU-Boulder)

## Slide 14: The current in an infinite solenoid with uniform magnetic field B inside is increasing so that the magnitude B in increasing with time as B=B0+kt. A small circular loop of radius r is placed coaxially inside the solenoid as shown. Without calculating anything, determine the direction of the field Bind created by the induced current in the loop, in the plane region inside the loop?
Into the screen
Out of the screen
CW
CCW
Not enough information
B
r
7.10
Notes: CORRECT ANSWER: A
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 15, Lecture 43)
STUDENT RESPONSES: [[95%]] 2% 2% 0% 0% (FALL 2008)
INSTRUCTOR NOTES: Flux rule for motional EMF
WRITTEN BY: Ed Kinney (CU-Boulder)

## Slide 15: The current in an infinite solenoid with uniform magnetic field B inside is increasing so that the magnitude B in increasing with time as B=B0+kt. A circular loop of radius r is placed coaxially outside the solenoid as shown. In what direction is the induced E field around the loop?
CW
CCW
The induced E is zero
Not enough information
B
r
7.11
Notes: CORRECT ANSWER: A
USED IN: Fall 2008 (Dubson)
LECTURE: Dubson (Week 15, Lecture 43)
STUDENT RESPONSES: [[81%]] 0% 16% 2% 0% (FALL 2008)
INSTRUCTOR NOTES: Flux rule for induced emf
WRITTEN BY: Ed Kinney (CU-Boulder)

## Slide 16: The current in an infinite solenoid with uniform magnetic field B inside is increasing so that the magnitude B in increasing with time as B=B0+kt. A circular loop of radius r is placed coaxially outside the solenoid as shown. Without calculating anything, determine the direction of the field Bind created by the induced current in the loop, in the plane region inside the loop?
Into the screen
Out of the screen
The induced B is zero
Not enough information
B
r
7.12
Notes: CORRECT ANSWER: A
USED IN:
LECTURE:
STUDENT RESPONSES:
INSTRUCTOR NOTES:
WRITTEN BY: Ed Kinney (CU Boulder)

## Slide 17: The current in an infinite solenoid with uniform magnetic field B inside is increasing so that the magnitude B in increasing with time as B=B0+kt. A small circular loop of radius r is placed outside the solenoid as shown. What is the emf around the small loop?
kπr2
-kπr2
Zero
Nonzero, but need more information for value
Not enough information to tell if zero or non-zero
B
r
7.13
Notes: CORRECT ANSWER: C
USED IN:
LECTURE:
STUDENT RESPONSES:
INSTRUCTOR NOTES: There’s no magnetic flux through the loop.
WRITTEN BY: Ed Kinney (CU Boulder)

## Slide 18: EMF I
Consider two situations: 1) loop moves right at velocity V(loop), and 2) magnet moves left, V(mag). Assuming |V(loop)| = |V(mag)|, what will the ammeter read in each case? (Call CW current positive)
h
B
A
I1 > 0, I2 = 0
I1 < 0, I2 = 0
I1 = I2
I1 = -I2
I1 = 0, I2 = 0 (special case)
7.1
Notes: 18
CORRECT ANSWER: C
USED IN: Spring 2008 (Pollock)
LECTURE NUMBER: 42
STUDENT RESPONSES: 0% 6% [[88%]] 6% 0%
INSTRUCTOR NOTES: End of class, 88% correct. It was a little rushed at the end, I didn't get much discussion from them.
This was my introduction to Faraday, I tried to argue that without Faraday, you'd have answer B (no reason for current to flow in situation 2, but qvxB would make it flow (CCW) in situation 1.
I "reused it" (without clicking) in the last lecture, it's a great example to discuss "there no E in the reference frame of the magnet, but there IS an E in the reference frame of the coil". One student wanted to understand how to think about it in terms of flux, it would be a good one to come back to if we had time to really get into Faraday... Ans: C. (Relativity?) -SJP
WRITTEN BY: Steven Pollock (CU-Boulder)

## Slide 19: EMF II
Ans: C) I1 = I2
The same result! But different physical situations are physically:
the same
equivalent
different
h
B
A
7.1b
Notes: CORRECT ANSWER: B
USED IN:
LECTURE NUMBER: Skipped
STUDENT RESPONSES:
INSTRUCTOR NOTES: SP08 Skipped: (but discussed),(from ward.ppt),Ans B), different mechanisms (changing B field (flux) --> E field v. magnetic force on moving charges) but they give the same answer and are the same with a Lorentz Transformation. -SJP
WRITTEN BY: Steven Pollock (CU-Boulder)