Phys1110 Exam 2 Review:

Everything from Exam I!

- algebra, trigonometry, unit conversions,

- 1D Motion:

,   ,  graphs,  slopes

constant acceleration formulas: , etc

  - Vectors!  vector addition, vector components

2D Motion:

- Projectile Motion

treat x- and y-motions independently

ax = 0     (     vx = constant

ay = – g  (     vy = voy – g t , etc

- Circular Motion with constant speed v,

are toward the center (centripetal)

- Newton's Laws

NI:

NII:

NIII:

New material since Exam I

Force and motion problems with one or more bodies:

1) Draw Free-body diagram

2) Choose Coordinate system

3)

Friction f

- sliding friction:   f  = K N

- static friction:      0  <  f  <  fmax  = S N

Work and Energy

- work done by force F:  ,  work can be (+), ((), or zero

- Hooke's Law: Fspring = ( k x     (k = spring constant)

- work-energy principle:

- Definition of PE associated with conservative force F:

- PEgrav  =  m g h	PEelastic = (1/2) k x2

- If no sliding friction, so no thermal energy generated :  Emech   =   KE + PE   =   constant

- If sliding friction,   KE + PE + Ethermal = constant

- Power

Gravity

Newton's Universal Law of gravity:

Acceleration due to gravity

r = distance to center of planet

Orbits,  Kepler's laws

Know how to use conservation of energy to derive escape speed.

To prepare for Exam 2:

- Review Concept Tests, CAPA problems, Tutorial HW.  (Read question and try to remember reasoning that gets to the answer)

- When reviewing CAPA problems, know how to derive algebraic formula for answer.

- Prepare your formula sheet.

- Take the practice exam.

- It is no good to memorize answers. You have to understand and remember how you construct the answers.

# Text boxes

r

Planet

mass m,

in free-fall

mass M

R

distance measured from centers

a

ax = 0

ay = –g

F

F

m2

m1

r

a

a

v



vx

x

v

vo

y

r

FBA

vy

B

FAB

A