Currents make B-fields

We have seen that charges make E-fields:   .

Currents make B-fields according to the Biot-Savart Law:

where 0  = constant = 4(10–7 (SI units).

dB is the element of B-field due to the element of current I dl . dl is an infinitesimal length of the wire, with direction given by the current. The total B-field due to the entire current is   .  This can be a very messy integral!

This law was discovered experimentally by two French scientists (Biot and Savart) in 1820, but it can be derived from Maxwell's equations.

Example of Biot-Savart: B-field at the center of a circular loop of current I, with radius R.  Here the integral turns out to be easy.    (

We can replace the vector integral

with the scalar integral  because all of the dB's point in the same direction. .

The full field at all positions near a current loop requires very messy integrations, which are usually done numerically, on a computer.  The full field looks like this:

Another, more difficult example of the Biot-Savart Law: B-field due to a long  straight wire with current I.  The result of a messy integration is

This formula can be derived from a fundamental law called Ampere's Law, which we describe below.  The B-field lines form circular loops around the wire.

To get directions right for both these examples (B due to wire loop, B due to straight wire), use "Right-hand-rule II":  With right hand, curl fingers along the curly thing, your thumb points in direction of the straight thing.

Force between two current-carrying wires:

Current-carrying wires exert magnetic forces on each other.  Wire2 creates a B-field at position of wire 1.   Wire1 feels a force due to the B-field from wire 2:

(     .

force per length between wires =

- Parallel currents attract

- Anti-parallel currents repel.

"Going my way? Let's go together.

Going the other way? Forget you!"

Gauss's Law for B-fields

B-field lines are fundamentally different from E-field lines in this way: E-field lines begin and end on charges (or go to ( ).  But B-field lines always form closed loops with no beginning or end.  A hypothetical particle which creates B-field lines in the way a electric charge creates E-field lines is called a magnetic monopole.  As far as we can tell, magnetic monopoles, magnetic charges, do not exist.  There is a fundamental law of physics which states that magnetic monopoles do not exist.

Recall the electric flux through a surface S is defined as .  In the same way, we define the magnetic flux through a surface as .    Gauss's law stated that for any closed surface, the electric flux is proportional to the enclosed electic charge:

.   But there is no such thing as "magnetic charge", so the corresponding equation for magnetic fields is

This equation, which has no standard name, is one of the four Maxwell Equations.  It is sometimes called "Gauss's Law for B-fields".

Ampere's Law

Ampere's Law gives the relation between current and B-fields:

For any closed loop L,    , where Ienclosed  is the current through the loop L .

(It will turn out the Ampere's Law is only true for constant current I.  If the current I is changing in time, Ampere's Law requires modification.) Ampere's Law for steady currents, like Gauss's Law, is a fundamental law of physics.  It can be shown to be equivalent to Biot-Savart Law.

We can use Ampere's Law to derive the B-field of a long straight wire with current I.

B-field of a long straight wire:

L = imaginary circular loop of radius r

We know that B must be tangential to this loop; B is purely azimuthal; B can have no radial component toward or away from the wire.  How do we know this?  A radial component of B is forbidden by Gauss's Law for B-fields.  Alternatively, we know from Biot-Savart that B is azimuthal.   So, in this case, Also, by symmetry, the magnitude of B can only depend on r (distance from the wire): B = B(r).

(

Like Gauss's Law, Ampere's Law is always true, but it is only useful for computing B if the situation has very high symmetry.

B-field due to a solenoid.  solenoid = cylindrical coil of wire

It is possible to make a uniform, constant B-field with a solenoid.  In the limit that the solenoid is very long, the B-field inside is uniform and the B-field outside is virtually zero.

Consider a solenoid with N turns, length L, and n = N/L = # turns/meter

(  B-field inside  solenoid  is

Permanent Magnets

Currents make B-fields.  So where's the current in a permanent magnet (like a compass needle)?  An atom consists of an electron orbiting the nucleus.  The electron is a moving charge, forming a tiny current loop –– an "atomic current".  In most metals, the atomic currents of different atoms have random orientations, so there is no net current, no B-field.

In ferromagnetic materials (Fe, Ni, Cr, some alloys containing these), the atomic currents can all line up to produce a large net current.

In a magnetized iron bar, all the atomic currents are aligned, resulting in a large net current around the rim of the bar.  The current in the iron bar then acts like a solenoid, producing a uniform B-field inside:

Why do permanent magnets sometimes attract and sometimes repel?  Because parallel currents attract and anti-parallel current repel.

# Text boxes

I

I

^

r

r

d l

I2

I1

B

E

l

loop L

B = 0 outside

B

L

Side View

B uniform

inside

dB

I

R

B

dl

^

r

I

dl

dB

r

^

r

F

I1

F

I2

B

I

F

F

r

r

B

Bfrom I2

I

L

F

F

I2

I1

M

Impossible!

Yes!

OK !

B

I

r

loop L

I

End View:

B

I

I

atoms

cross-section of

magnetized iron bar

In interior, atomic currents cancel:

net I = 0

on rim, currents all in same direction, currents add

net atomic current on rim

uniform

B(out)

atomic current on rim,

like solenoid

Side View:

End View:

N

S

B-field comes

out of "North" end

B-field enters

"South" end

N

S

N

S

parallel currents on ends attract

opposite poles attract :

N

S

N

S

like poles repel :

anti-parallel currents

on ends repel

I(out)

I(in)