PHYS1120 Exam III review

Things to remember for PHYS1110:  algebra, trig (sin, cos, ..)

vector math, especially vector addition,  Fnet = ma problems, free-body diagrams

Exam1 and Exam2 Material :  E-fields, Gauss's Law, voltage, capacitors, circuits.

Last part of Chapter 26 :  RC circuits

- Voltage across a capacitor is always .

- An uncharged capacitor has V= 0 , acts like a wire, as short (does not resist the flow of current).

- A fully charged capacitor has I = 0, acts like an open switch.

- time constant is = RC

Ch. 27 Magnetic fields

(

(          This is the definition of B .

(   When both E-field and B-field are present:

(   Motion of charge in magnetic field and in velocity selector.

(   ,    force and torque on a current loop

Ch. 28 Sources of Magnetic fields

(   Currents cause magnetic fields (B-fields)

(   Biot-Savart Law:     (Know what all the symbols mean)

(   Ampere's Law:

Be able to use Ampere to derive

    - B-field outside long straight wire:   ,

    - B-field inside long wire:

    - B-field inside solenoid:

(No need to memorize these formulas; know how to derive them)

(   "modified right-hand rule"  point thumb in direction of straight thing, fingers curl in sense of circular thing.

(   B-field is a vector:

(  parallel currents attract; anti-parallel currents repel

(  Gauss's Law for B-fields:    (  Magnetic monopoles do not exist.

( field of a solenoid,   permanent magnet acts like solenoid

Ch. 29 Faraday's Law

( Faraday's Law: An emf (= battery voltage) is caused by a changing magnetic flux:

( where  is the flux through 1 loop)

magnetic flux ,   emf around a loop

Be able to use Faraday's Law to derive E-field inside or outside a solenoid.

( Lenz's Law: Iinduced creates Binduced in direction that opposes the change in flux.

( Motors and generators

( Eddy current forces always oppose the motion

To prepare for any exam:

- Study my online lecture Notes.

- Review Concept Tests,  CAPA problems, and Tutorial HW.  (Read question and try to remember reasoning that gets to the answer)

- Prepare your formula sheet.  Prioritize: which are the important equations?

- Take the practice exam.

- It is no good to memorize answers.  You have to understand and remember how you got the answers.

# Text boxes

B-field enters

"South" end

B-field comes

out of "North" end

S

N

End View:

Side View:

atomic current on rim,

like solenoid

uniform

B(out)

net atomic current on rim

B

I