PHYS1120 Exam II review

Things to remember for PHYS1110:  algebra, trig (sin, cos, ..)

vector math, especially vector addition,  Fnet = ma problems, free-body diagrams

Exam I Material :  E-fields, Gauss's Law

Chapter 23  Voltage = Electric Potential

- Definition of voltage:    ,

- (    ( if E = constant and  ) ,

- Voltage is electrical height, E-field is slope

- if ,   , equipotential lines

- Voltage due to a point charge Q:

- Voltage due to many charges:

- Work done by external agent to move charge q through a voltage differenceV =  . If charge q falls through a voltage differenceV,

- Units of electron volts (eV).

Ch.24 Capacitors

(   capacitance

(   C depends only on size and shape:

(  Adding capacitors in series and parallel.

(   stored energy =

(   energy per volume =  .

Ch.25, 26 Current and Circuits

(  ,        (where n = #carriers/volume, vd = drift speed)

,   = resistivity = measure of internal friction, depends on composition

(   Ohm's Law:

(   Resistance of a resistor:

(

(   Equivalent Resistance:

Things that are always true in circuits:

(   elements in series always have the same current:

(   elements in parallel always have the same voltage:

(   voltage change along an unbroken ideal wire is zero (since we assume Rwire = 0 ) :

(   ideal battery means constant V  for any current, current depends on the circuit

(   K's Current Law (Junction Law)

total current into junction  = total current out of junction  :

(   K's Voltage Law (Loop Law): total voltage change around any closed loop is zero

(   Ammeters and Voltmeters

To prepare for Exam 1:

- Review Concept Tests,  CAPA problems, and Tutorial HW.  (Read question and try to remember reasoning that gets to the answer)

- Prepare your formula sheet.

- Take the practice exam.

- It is no good to memorize answers.  You have to understand and remember how you got the answers.

# Text boxes

lo V

hi V

E

+Q

–Q

E

V = V

area A

d

R

I

V

hi V

lo V

area A

L

in series:

R1

R2

=

Rtot = R1 + R2

R1

R2

=

in parallel:

Rbig

Rsmall

Ismall

Ibig

V same

across both R's

R1

R2

I

I

R3

I

I

V

I2

I3

I1

I1

junction

junction

d