RC Circuits

An RC circuit is a circuit with a resistor (R) and a capacitor (C).  RC circuits are used to construct timers and filters.

Example 1.  Very simple RC circuit: a capacitor C, charged to an initial voltage V0 = Q0/C, attached to a resistor R with a switch.

Close the switch at time t = 0 , so current I starts to flow.  The charged capacitor is acting like a battery: it produces a voltage difference across the resistor which drives the current through the resistor:

At t = 0+,      .

(– sign because Q is decreasing)

Vacross C  =  Vacross R ,  VC  = VR ,  ,   ,

RC = "time constant" =   , has units of time

is a differential equation of the form  ,   where a is a constant.

This equation says: (rate of charge of x) (  x   (   exponential solution :

Check:  .    It works!

a  >  0   (  exponential growth ,     a  <  0   (  exponential decay

The solution to     is

Notice that at t = 0, the formula gives Q = Q0 .

In time  , Q falls by a factor of exp(–1) = 1/e  (  0.37..

In time 2, Q falls by a factor of exp(–2) = (1/e)(1/e) (  0.14..

( Q approaches zero asymptotically, and so does V and I

Example 2: More complex RC circuit:  Charging a capacitor with a battery.

Let's use symbol E for  battery voltage (E short for emf) because there are so many other V's in this example.

Before switch is closed, I = 0, Q = 0.

Close switch at t = 0.

Always true that  E  =  VC + VR  ,

by Kirchhoff's Voltage Law (Loop Law)

The charge Q on the capacitor and the voltage VC = Q / C across the capacitor  cannot change instantly, since it takes time for Q to build up,  so ..

At t = 0+ , Q = 0 , VC = 0,  E = VC + VR = VR = I R   (  I0 = E / R

Although Q on the capacitor cannot change instantly, the current I = dQ/dt can change instantly.

"Current through a capacitor"  means dQ/dt .  Even though there is no charge ever passing between the plates of the capacitor, there is a current going into one plate and the same current is coming out of the other plate, so it is as if there is a current passing through  the capacitor.

Qualitatively, as t ( ,  Q ( ,  VC = Q/C  ( , VR ( ,  I = VR / R (.  After a long time , t >> = RC , the current decreases to zero:  I = 0, VC = E , Q = C E

Analytic solution:

Things to remember:

- Uncharged capacitor acts like a "short" ( a wire ) since VC = Q / C = 0.

- After a long time, when the capacitor is fully charged, it acts like an "open-circuit" ( a 	break the wire).  We must have IC = 0 eventually, otherwise Q (  ( , VC  (  ( .

# Text boxes

switch

E

t

t

V = Q / C



Q0/e

Q0

t

Q

R2

R

–Q0

+Q0

C

I

–Q

+Q

switch

C

R

VR = I R

C

R

VC = Q / C

I

I

+

+

+

+

-

-

-

-

I

E

E

C

R

t

Vc = Q / C