Phys2010 Exam 3 Review:

Chapter 6:  Work and Energy

- work done by force F:  ,  work can be (+), ((), or zero

- work-energy principle:

- If no thermal energy generated,   Emech   =   KE + PE   =   constant

- If thermal energy generated,   KE + PE + Ethermal = constant

- Hooke's Law: Fspring = ( k x     (k = spring constant)

- PEgrav  =  m g h	PEelastic = (1/2) k x2

- Power

Chapter 7:  Momentum

- Conservation of momentum: for system isolated from outside forces,

- Impulse  =

- elastic vs. inelastic collisions.  KE is conserved only in perfectly elastic collisions.

Chapter 8:  Rotations

Notice analogy between rotation about a fixed axis and 1D translation along the x-axis:

- ( like )

- v  =  r    ,   atan   =   r 

- torque

- moment of inertia

- net  =  I ( like Fnet = m a )

- KErotation  =  (1/2) I 2       ( like KEtrans  =  (1/2) m v2)

- Rolling motion: KEtot = KEtrans + KErot =

- Angular momentum L = I   (like linear momentum p = mv )  Angular momentum of an isolated system is conserved.

Remember:  to solve any before/after problem, try conservation of energy or conservation of momentum or conservation of angular momentum.  Energy or momentum or angular momentum only conserved if system is isolated.

- Conservation of linear momentum useful for collision problems, even if thermal energy is generated.  Momentum is conserved regardless of whether collision is elastic or inelastic.

- Conservation of mechanical energy (KE + PE ) useful only if no sliding friction or inelastic collisions, so no thermal energy generated.

- Conservation of angular momentum useful for isolated rotating systems

To prepare for Exams:

- Review Concept Tests and CAPA problems.  (Read question and try to remember reasoning that gets to the answer)

- Prepare your formula sheet.

- Take the practice exam.

- It is no good to memorize answers.  You have to understand and remember how you construct the answers.