Transformed E&M I homework

Boundary Value Problems

(Griffiths Chapter 4)

Boundary value problems

Question   Cubical box filled with dielectric

CALCULATION; BOUNDARY VALUE (U. Nauenberg, HW6, solutions available)

Consider a cubic box made up of dielectric material with a dielectric

constant ǫ. The length of each side is “a”. The boundary conditions are

specified in terms of the electric field as follows:

Ex = 0 at the surfaces defined by x = 0 and x = a.

Ey = 0 at the surfaces defined by y = 0 and y = a.

Ez = 0 at the surface defined by z = 0 and Ez = E0 (x, y) at z = a.

Find the potential everywhere inside the box in terms of E(x, y).

Question   Dielectric sphere in E field

CALCULATION; BOUNDARY VALUE (U. Nauenberg, HW8, solutions available)

A solid dielectric sphere of radius “a”, with dielectric constant epsilon̨, has

a uniform free surface charge/unit area σ is placed in an initially uniform

electric field E0 pointing in the z direction.

(a)Calculate the potential everywhere.

(b)Calculate the E field everywhere.

(c)Calculate the distribution of the polarization “P” in the sphere and the

surface and volume bound charge distribution.