Exam III review.

CT3-1

An electron and a proton have the same momentum (p=mv) and enter a region where there is a uniform magnetic field.  Which particle is bent more?

A: electron	B: proton	C: both are bent the same amount

CT3-2

A charged particle is orbiting in a uniform B-field in the sense shown.

Is the particle positive or negative?

A: positive

B: negative

C: impossible to tell

CT3-3

A coil of wire carrying current I can rotate freely about an axis in a magnetic field.  If released from rest in the position shown, which way does it rotate?

A: right side will move out of page

B: left side will move out of page.

C: loop will not rotate at all

CT3-4

A long U-shaped wire carries a current I in the sense shown.  Consider the magnetic field B at the point A, which is equi-distant from the two corners of the U and in the same plane as the U.  Which one of the following statements is true?

A:  B has a z-component only which is due entirely to the bottom segment of the U.

B: B has a z-component only which has contributions from the bottom and sides of the U.

C: B has a non-zero x-component, as well as a z-component.

D: B has a non-zero y-component, as well as a z-component.

CT33-5.

A long U-shaped wire carries a current I in the sense shown.  Consider the (imaginary) loop of radius r centered on the right side of the U as shown.  True or False?  For the loop shown, .

A: True		B: False.

True or False? At point A, the magnitude of the magnetic field is .

A: True		B: False.

CT3-6

Consider the following configuration of B-field lines (solid lines) and the imaginary rectangular loop (dotted line).  Which one of the following statements is true?

A: There must be a non-zero current thru the imaginary loop going into the page.

B: There must be a non-zero current thru the loop coming out of the page.

C:  There is no current going thru the loop.

CT3-7.   A bar magnet with the ends properly labeled N and S is placed near an unlabeled bar magnet as shown.  The magnets attract.  The left side of the unlabeled bar magnet must be a

A: South pole			B: North pole

CT3-8

A  circuit with a battery and a variable resistor is near a loop of wire as shown.  When the resistance R is decreased, the induced current in the loop is ..

A: CW

B: CCW

CT3-9  A metal bar (not attached to any outside circuitry) is moving through a uniform magnetic field as shown.  The electric field E within the bar is ..

A:  non-zero and downward (

B: non-zero and upward (

C: zero

CT3-10

A solenoid has an increasing current which creates an increasing B-field in its interior.

The electric field at point c is

A: up (

B: down (

C: left (

D: right (

E: zero

At which of the three points (a, b, or c) is the E-field maximum?

A: a		B: b		C: c

D: the E-fields at b and c have the same magnitude and are larger than the E-field at a.

CT3-11 A uniform solid sphere of copper rotates about a stationary axis in a uniform magnetic field B.  Are there eddy currents?

A: Yes, there are eddy currents.

B: No, no eddy currents.

CT3-12  The switch in the circuit below has been closed for a long time and then is opened at t=0. What is the current in the inductor at t=0+?

A: zero

B: 1A

C: 0.5A

D: some other answer

At t=0+ , what is the current through resistor R2?

A: zero	B: 1A		C: 0.5A	D: some other answer

At t=0+, what is the voltage across the capacitor?

A: zero		B: not zero.

At t=0+,  energy that originally came from the battery is now in the right half of the circuit in what forms?

A: magnetic field energy only

B: thermal energy only (the resistor is hot)

C: electric field energy only

D: some combination of these three forms of energy

If the inductance L was doubled (20H instead of 10H), then at t=0+, the magnetic field energy would be..

A: the same as before	B: twice as large

C: 4 times as large.  	D: some other answer

CT3-13.

A 600W hairdryer is attached to 120VAC circuit.  What is the peak current through the hairdryer (to within 5%)?

A: 10A		B: 7A		C: 5A

CTIII-14

A step-up transformer is plugged into a standard 120 VAC wall socket.  The secondary of the transformer is attached to a variable resistor R.

As R is reduced, the voltage Vs across R..

A: remains the same.		B: decreases.		C: increases.

As R is reduced, the current through R..

A: remains the same.		B: decreases.		C: increases.

As R is reduced, the power drawn from the wall socket..

A: remains the same.		B: decreases.		C: increases.