CAPCT-0

Free question:

I thought Exam I was

A) too easy	B) about right	C) too hard.

CAPCT-

A parallel-plate capacitor has square plates of edge length L, separated by a distance d.  A second capacitor is made with L doubled and d decreased by a factor of 2.

By what factor is the capacitance of the new capacitor increased?

A: 1 		B: 2		C: 4		D: 16		E: None of these.

CapCT- A parallel-plate capacitor with capacitance C has a charge Q (meaning +Q on one plate, -Q on the other).  The charge is doubled to 2Q (meaning +2Q on one plate, -2Q on the other).  The capacitance C of the capacitor...

A) doubled		B) decreased by 2X	C) remained constant

D) None of these

CAPCT-  A parallel-plate capacitor is charged up (+Q on one plate, -Q on the other).  The plates are isolated so the charge Q cannot change.  The plates are then pulled apart so that the plate separation d increases.  The total electrostatic energy stored in the capacitor

A: increases

B: decreases

C: remains constant.

CAPCT-   A parallel plate capacitor is attached to a battery which maintains a constant voltage difference V between the capacitor plates.  While the battery is attached, the plates are pulled apart so their separation increases. The electrostatic energy stored in the capacitor

A: increases

B: decreases

C: stays constant.

CT25-   A positive charge +Q and a negative charge –Q are held a distance R apart and are then released. The two particles accelerate toward each other as a result of their coulomb attraction.  As the particles approach each other, the energy contained in the electric field surrounding the two charges..

A: increases		B:  decreases	C: stays the same.

CAPCT-

Consider a capacitor made of two isolated parallel metal plates separated by a distance d.  The top plate is positively charged with total charge +Q; the bottom plate is negatively charged with total charge –Q.  A slab of metal of thickness t < d is inserted between the plates, not connected to either one.  Upon insertion of the metal slab, the voltage difference between the top and bottom plates.  [Hint: (V = E d ]

A: increases		B: decreases		C: remains constant.

Another hint: The charge density, before and after, looks like:

After insertion of the third plate, the ratio Q/V where Q is the charge on the top plate and V is the voltage difference between top and bottom plates..

A: increases		B: decreases		C: remains constant.

CAPCT-

Two capacitors C1 and C2  are hooked in series.  The equivalent series capacitance of the two capacitors is …

A: Always less than C1 or C2

B: Always greater than C1+C2

C: Always greater than C1 or C2 but always less than C1+C2

D: None of these.

CAPCT-

A parallel-plate capacitor with a dielectric between the plates is charged so that +Q resides on one plate, –Q on the other.  With the plates isolated and the charge Q constant, the dielectric is pulled out from between the plates. The energy stored in the capacitor ...

A: increased		B: decreased		C: stayed the same.

Hint: Was work done when the dielectric was removed?

Same question, except now the capacitor is hooked to a battery which maintains a constant voltage between the plates as the dielectric is removed.

The energy stored in the capacitor ...

A: increased		B: decreased		C: stayed the same.

With the voltage fixed, as the slab was removed, the charge Q on the capacitor ..

A: increased		B: decreased		C: stayed the same.