CrktCT -9. The three light bulbs A, B, and C are identical.  How does the brightness of bulbs B and C together compare with the brightness of bulb A?

A)  Total power in B+C = power in A.

B) Total power in B+C > power in A.

C) Total power in B+C < power in A.

Answer:  Use P = V2/Rtot    For bulbs B and C, Rtot = 2R.

Total power in B+C < power in A.

CrktCT -10.  Two light bulbs A and B are connected in series to a constant voltage source. When a wire is connected across B as shown, the brightness of bulb A ...

A:	increases

B:	decreases, but remains glowing

C:	decreases to zero (bulb A goes completely dark, no current)

D:	remains unchanged

Answer: Bulb A increases in brightness (since the current increases when B is shorted).

CrktCT -11.

A circuit with two batteries is shown below.  The directions of the currents have been chosen (guessed) as shown.

Which is the correct current equation for this circuit?

A) I2 = I1 + I3 		B) I1 = I2 + I3		C) I3 = I1 + I2		D)  None of these.

Answer: I3 = I1 + I2

CrktCT -12.

Which equation below is the correct equation for Loop 1?

A) –V2 + I1R1 – I2R2 = 0		B) V2 + I1R1 – I2R2 = 0

C)   –V2 – I1R1 + I2R2 = 0		D) V2 + I1R1 + I2R2 = 0

E) None of these.

Answer: –V2 + I1R1 – I2R2 = 0

CrktCT -13. Consider the circuit shown.  If you want to measure the current thru bulb 3, how should the ammeter be attached?

A) Pink		B) Yellow		C) Green		D) Blue

E) Two of the 4 positions can be used to measure bulb3’s current.

Answer: B) Yellow

CrktCT -14. I)  In the circuit shown, what does the voltmeter read?

A:  	6 V

B:  	3 V

C:  	2 V

D:	0 V

E:   	Voltmeter will "fry"

Answer: 6 V

Now you switch the voltmeter over to "amp" mode.

(But you leave it in the same position in the circuit)

What does the ammeter read?

A:  	6 A

B:  	3 A

C: 	2 A

D:	0 A

E:  	Ammeter will "fry"

Answer: Ammeter will fry.  Ideal ammeter has zero internal resistance.  If you attach an ideal ammeter to a battery, you will get infinite current.

CrktCT -15. The light bulbs in the circuit are identical. When the switch is closed,

A: bulb A glows, and bulb B changes brightness

B: bulb A glows, and bulb B stays the same

C: bulb A does not glow, and bulb B changes brightness

D: bulb A does not glow, and bulb B stays the same

E: Something else happens

Answer: bulb A does not glow, and bulb B stays the same

After the switch is closed, the voltage drop across bulb A is zero, while the voltage drop across B is 12V

CrktCT -16.

The light bulbs in the circuit are identical. When the switch is closed,

A:both go out.

B:both stay the same

C:the intensity of light bulb B increases.

D:the intensity of light bulb B decreases.

E: both bulbs burn out due to infinite (very large) current

Answer:  both stay the same.

CrktCT -17.

All batteries shown are identical (1.5 V)

How do the brightnesses of the bulbs compare?

(Look carefully at the orientation of the batteries!)

A: A is brighter

B: A and B are the same brightness

C: A is on, but B is brighter

D: A is off, so B is brighter

E: Both bulbs are off

Answer: A and B are the same brightness, since both have the same voltage across them.  In A, two of the three battery voltages cancel.

CrktCT -18. In the circuit shown,  the two bulbs are identical.

The switch is suddenly closed. What happens to the currents through points A and B?

A:  IA stays same, 	IB decreases

B:  IA increases, 	IB stays the same

C:  IA stays same, 	IB stays the same

D:  IA increases,	IB decreases

E:  IA decreases, 	IB decreases

Answer:  IA increases,  IB stays the same