F-10 An electric motor consists of a coil, free to turn on an axis, and located in an magnetic field B created by an arrangement of permanent magnets.  With the current and field directions as shown, which way will the coil rotate?

A: CW

B: CCW

C: the coil won't rotate when at this particular orientation

Answer: CCW

F-11  A solenoid has an increasing current causing an increasing B-field in its interior.   An end-on view of the solenoid is shown below.  An electron is directly below the solenoid.  While the current I in the solenoid is increasing, what is the direction of the force on the electron?

Hint: What is the direction of the E-field at the position of the electron?  Think Lenz's Law.

Answer: the force on the electron will be left (,  the E-field will be right (.

By Faraday's Law, the changing flux through any loop centered on the coil will cause an emf  .  By Lenz's Law, the direction of the E-field will be such as to tend to cause a current which opposes the change in flux.  In this case, the E-field will circulate CCW to tend to create a CCW current, which will create an induced B-field out of the page, to fight the flux change.  Since the electron has a negative charge,  the force is in the direction opposite the E-field.

F-12  A long solenoid of radius R contains a uniform magnetic field B which is increasing at a steady rate [B(t) = A t,  where A is a constant].  For distances r < R from the center of the solenoid, how does the  magnitude of the Electric field depend on r?  Hint:

A: E = zero

B:  E ( 1/r

C: E ( r

D: E ( r2

E: E ( r3

Answer: E ( r, inside the solenoid.  ( E ( 1/r outside the solenoid.)

For any loop of radius r centered on the solenoid, we can argue that  , due to symmetry.  For loops within the solenoid,  , which leads to E ( r, inside.

For loops outside the solenoid, = independent of r, which leads to E ( 1/r.

# Text boxes

axis

B

B

I

B

A

B(in)

A

B

D

C

electron