Faraday CT's

F-

A square loop of area A is in a constant uniform magnetic field.

In which situation is the magnetic flux through the loop the smallest?

F- A loop of wire is moving rapidly through a uniform magnetic field as shown.

True (A) or False(B): there is a non-zero emf induced in the loop.

F- A loop of wire is spinning rapidly about a stationary axis in uniform magnetic field as shown.

True(A) or False(B): there is a non-zero emf induced in the loop.

F- The magnetic flux through a loop of wire is shown.  At which point is the magnitude of the emf induced in the loop a maximum?

F- A loop of wire is sitting in a uniform, constant magnet field  as shown.  Suddenly, the loop is bent into a smaller area loop.  During the bending of the loop, the induced current in the loop is ...

A: zero		B: clockwise			C: counterclockwise

F- A bar  magnet is  positioned below a horizontal loop of wire with its North pole pointing toward the loop.  Then the magnet is pulled down, away from the loop.  As viewed from above, is the induced current in the loop clockwise or counterclockwise?

F- A square loop is rotating in a fixed, external magnetic field into the page.  At the instant shown, the loop is out of the plane of the page with left side of the loop above the page and coming out of the page, the right side in going in.  The direction of the induced current is ...

F-  A loop of wire is near a long straight wire which is carrying a large current I, which is decreasing.  The loop and the straight wire are in the same plane and are positioned as shown.  The current induced in the loop is

A: counter-clockwise		B: clockwise		C: zero.

F-  Two loop of wires labeled A and B are placed near each other as shown.  A large current I in loop A is suddenly turned on.  This causes an induced current in loop B which causes

A: A net replusive force - the two loops repel

B: A net attractive force - the two loops attract

C: whether the force is attractive or repulsive depends on whether the current in first loop is CW or CCW

D: No net force.

F-  A wire loop, moving right, enters a region where there is a constant, uniform magnetic field pointing into the page.

As the loop enters the B-field, the current induced in the loop is ...

A: CW		B: CCW

As the loop enters the B-field, the direction of the net force on the loop is ...  A: right (		B: (		C: up (	D: (down

E: there is no net force

F-   The vertical wire shown is moving to the right in a uniform magnetic field which is into the page.  There is a current upward, meaning that there is a flow of electrons downward.  The fixed positive ions in the wire are moving to the right, along with the wire. The negative conduction electrons are moving to the right and down.  What is the direction of the net magnetic force on this segment of the wire?

A) Up 	B) Down 	 C) Left	D) Right	E) None of these

F- An electric motor consists of a coil, free to turn on an axis, and located in an magnetic field B created by an arrangement of permanent magnets.  With the current and field directions as shown, which way will the coil rotate?

A: CW

B: CCW

C: the coil won't rotate when at this particular orientation

F-  A solenoid has an increasing current causing an increasing B-field in its interior.   An end-on view of the solenoid is shown below.  An electron is directly below the solenoid.  While the current I in the solenoid is increasing, what is the direction of the force on the electron?

Hint: What is the direction of the E-field at the position of the electron?  Think Lenz's Law.

F-  A long solenoid of radius R contains a uniform magnetic field B which is increasing at a steady rate [B(t) = A t,  where A is a constant].  For distances r < R from the center of the solenoid, how does the  magnitude of the Electric field depend on r?

Hint:

A: E = zero

B:  E ( 1/r

C: E ( r

D: E ( r2

E: E ( r3

F-  A transformer is connected to a battery as shown. The voltage difference across the resistor R is ...

A)  V N2/N1		B) V N1/N2		C) V

D) zero.		E) not enough information to answer.

F- The primary coil of a transformer is connected to a battery, a resistor, and a switch.  The secondary coil is connected to an ammeter.  When the switch is thrown closed, the ammeter shows..

A)   a zero current all the time

B)  a non-zero current for a brief time when the switch is closed

C)  a steady non-zero current after the switch is closed

F-  A step-down transformer is attached to an AC voltage source and a resistor as shown.  How does the current in the resistor I R compare to the current in the drawn from the AC source Iinput?  (With AC circuits, we always use rms values of I and V.)

A) I R  >  I_in

B) I R  <  I_in

C) I R  =  I_in

D) Depends on the value of Iin

F-  An electrical engineer at a power plant wants to reduce the energy wasted during power transmission from the plant to the city.   The power output Po=IV of the plant is fixed at 100MW.  The engineer decides to double output voltage V.   By what factor does the power lost in the cable (Plost = I2 Rcable) decrease?  (Hint: if P=IV is fixed, when V goes up, I goes down.)

A) No decrease			B) factor of 2 decrease

C) factor of 4 decrease	D) factor of 8 decrease

F-  A long, straight wire carrying an increasing current I passes along a diameter of a wire loop.  The straight wire and the loop are in the same plane but are not in electrical contact.

The induced current in the loop is:

A)  zero.

B)  counter-clockwise

C)  clockwise.

F-  A rectangular loop is placed in a uniform magnetic field with the plane of the loop perpendicular to the direction of the field.  If a current is made to flow through the loop in the sense shown by the arrows, the field exerts on the loop...

A) a net force only

B) a net torque only

C) a net force and a net torque

D) neither a net torque nor a net force.

# Text boxes

loop

axis of rotation

area A

tilted 60°

C) Neither

area A

face-on

iron

core

axis

C

B

A: clockwise

B: counter-clockwise

N

S

eyeball

B(in)

A

B

B

B

I

B

A

area A

edge-on

(C)

(B)

(A)

constant,

uniform

B-field

B

A

A

D

motion of

conduction electrons in wire

flux (

motion of wire and

of fixed positive ions

time

electron current

conventional current I

B(in) uniform

V(AC)

I increasing

I

B

IR

I_in

B(in)

B(in)

I to the right, but decreasing.

V

R

N1

N2

R

iron core

V

Rcity

(adjusted to keep

P=IV constant.)

I

Rcable

loop

No electrical contact between

loop and straight wire.

B

r

R

electron

C

D

B

A

B(in)

(D) Same flux in all three situations