Concept Tests -- Final Review

CTF-A square with edge length L is made larger and larger...

As the square grows, the ratio ..

A) increases		B) decreases		C) remains constant.

CTF- A box with mass M and charge +Q is pushed along a rough surface at constant velocity by a uniform horizontal electric field of magnitude E.  The coefficient of kinetic friction between the box and the floor is .  What is the net force on the box?

A) QE	B) g	C) zero	D) QE – Mg + FN –  Mg .

E) None of these

CTF-

Points A and B are distances r and 3r respectively from a point charge q.  What is the voltage difference between points A and B?

A)		B) 	C)  		D) 	E) None

CTF- Consider a point in empty space near several charges, which might be positive, negative, or both.  Consider the following statements.

I. The E-field can be zero while the voltage is non-zero.

II. The voltage can be zero while the E-field is non-zero.

Which of these statements can be true?

A) both can be true		B) neither can be true

C) only I can be true		D) only II can by true

CTF- A capacitor has a voltage V across its plates.  An electron, initially at rest, is released from a point very close to the negative plate of a capacitor and it accelerates toward the positive plate.   The electron has charge –e and mass m.  There is no gravity in this problem, and you may assume that the motion of the electron is non-relativistic.  What is the final kinetic energy of the electron just before it collides with the positive plate?

A) 		B) 2eV

C) (1/2)mV2		D) eV

E) None of these

CTF-  A resistor is plugged into a 120VAC wall socket.  The graph below is either voltage V across, current I thru, or power P dissipated in the resistor vs. time.

What could the graph be?

A) V only		B) I only	C) V or I only	D) V, I, or P

CTF- Consider the circuit shown, with the switch initially open. When the switch is closed, the current I1 through resistor R1

A) increases, 	B) decreases,

C) stays the same.

Answer: stays the same.  I1 = V/R1 regardless of whether or not the switch is closed.  What does change is the battery voltage.

CTF-  When the switch is closed, the current from the battery Ibat

A) increases, 	B) decreases, 		C) stays the same.

CTF-  When a resistor is plugged into a standard AC outlet, the fuse blows and all the lights go out.  If we want to repeat this dangerous experiment, and not have the fuse blow,  we need a resistor that is

A) larger		B) smaller

C) Same R, but larger power rating

CTF-  A charge q is released from rest at point in empty space were there may be E- and/or B-fields.  There are no forces on the charge except for the forces due to the E and/or B-fields (no gravity, etc.).  The charge is observed for a short while and is seen to move along a curved path.

Consider the following possibilities

I. There is only an E-field present and no B-field.

II. There is only a B-field present and no E-field.

III. There is both an E-field and a B-field present.

Which possibilities could account for the observed motion?

A) all three 	B) I and III only		C) II and III	D) III only

CTF-  At time to, a particle with charge q has instantaneous velocity as shown and is moving in a uniform magnetic field .

A) True	or   B) False  ?

As time increases, the x-component of the velocity vx remains constant.

CTF- A horizontal loop of wire is in a vertical magnetic field.  The magnetic field varies smoothly from pointing upward to pointing downward, as shown. (The B-field gradually gets smaller, goes to zero, then grows in the other direction.)

At the moment when the magnetic field in the loop is zero, is there an induced current in the loop?

A) Yes		B) No

CTF- What is the direction of the induced current?

A) Clockwise (as seen from above)	B) Counterclockwise

CTF-  An radio tower is emitting a single-wavelength (monochromatic) EM wave in all directions (isotropically).  A technician measures the electric field amplitude E at 100 meters from the tower and again at 400m from the tower.  
The intensity of an EM wave is proportional to the square of the amplitude of the E-field: I ( E2.  What is the ratio E100/E400?

A) 2		B) 4		C) 16	 	D) 162 = 256

Answer: 4  The intensity is 16 times greater at 100 m than at 400 m, but the E-field is only 4 time greater.

CTF-  A head lamp of power P sends rays of light in the forward direction only.  At a distance R in front of the lamp, the intensity of the light is _________    (fill in the blank)

A) greater than		B) less than	C) equal to

CTF-  Is the image formed by the lens in your eye real or virtual?

A) real 		B) virtual

CTF- A double slit interference pattern is seen on a screen

The path difference (p.d.) for a given point on the screen is the quantity [(distance to slit 1) - (distance to slit 2)].

What is the path difference at point A?

A) 5(		B) 3(		C) 2(	D) None of these

CTF-  An observer stationary on the Earth sees a rocket moving to the right at speed v = 0.75 c.  The rocket has a tail light on its back which emits a flash of light to the left. According to the Earth observer, the light beam and the rocket are moving apart with a relative speed of  …

A) c

B) 1.75 c

C) 0.25 c

D) 0

E) None of these

(Relative speed means how fast the distance between the light beam and the rocket is increasing.)

CTF- The rest mass energy of an electron is  .    An electron is accelerated from rest across a voltage V.  At what voltage V is the final kinetic energy of the electron equal to its rest mass energy?

A) V=0.511 MV		B) 1.022 MV		C) 1.533 MV

D) None of these.

# Text boxes

v = 0

light beam

v = (3/4) c