CT18-1

The instructor goes crazy and grabs the terminals of a fully-charged 12V battery.  He will..

A) immediately be killed.

B)  not be killed, but he will start hollering because it really hurts.

C) not feel anything.  This action is harmless.

Answer: He will not feel anything. His body's resistance R is very large (mega-ohms), so the current through him (I = V/R) is very small.

CTR-

Which graph of voltage vs. current shows the behavior of an "ohmic" resistor (a resistor obeying Ohm's Law).

18-2.

Two cylindrical resistors are made of the same material (same resistivity ().  Resistor 2 is twice as long and has twice the diameter of resistor 1.  What is the ratio  (The arrow shows the direction of current flow.)

A) 2			B) 4

C) 1/2			D) 1/4

E) 1

Answer: The ratio is 1/2.  .  The area is proportional to (radius)2 or (diameter)2.  When the diameter is doubled, the area increases by a factor of 4.

18-3.

A battery with emf or voltage V is attached to a resistor of resistance R.  The circuit diagram is shown below.  The point A is at zero volts.

The correct voltages at the points B, C, and D are:

A) 	VB = 0V,  VC = 5V,  VD = 0V.

B)	VB = 5V,  VC < 5V,  VD  >  0V.

C)	VB = 5V,  VC < 5V,  VD = 0V.

D)	VB = 5V,  VC = 5V,  VD = 0V.

E) 	None of these.

Answer: VB = 5V,  VC = 5V,  VD = 0V.  As you move along a wire, there is no voltage change.

18-4.

A light bulb is attached to a battery with constant voltage V.  The light filament has resistance R.  The circuit diagram is shown below.  When the light bulb is first turned on by attaching to the battery, the filament heats rapidly, and as it heats, its resistance R increases (due to increased scattering of electrons by thermal vibrations).

As the light bulb filament heats up, the current I in the filament ...

A) increases 		B) decreases		C) stays the same.

Answer: I decreases.  I = V/R.  As R increase, I decreases.

CT18-5 What is the correct way to connect the battery to the lightbulb to make it light up?

Answer:  Circuit (B) is the only one that will work.

CT18-6.

A 60W light bulb and a 100W light bulb each has a filament with a certain resistance (when the bulb is on and hot).   How do the resistances of the filaments compare?

A) R60W = R100W.	B) R60W > R100W

C) R60W < R100W	D) Impossible to tell without further information.

Hint: P = V2/R

Answer: R60W > R100W.  Lightbulbs are labeled with the wattage they will have when a voltage of 120 VAC is applied.  100W bulbs have more power (when 120VAC is applied) than 60W bulbs.  From P = V2/R, we see that smaller R results in bigger P.

CT18-7.

Please answer now.

The voltage provided by your household wall sockets is....

A) AC voltage

B) DC voltage

C) Depends on the appliance which you plug into the socket.

Answer:  Household line voltage is 120 VAC.

CT-18-8

Two light bulbs, A and B, are in series, so they carry the same current.  Light bulb A is brighter than B.  Which bulb has higher resistance? (HINT: brighter means more power.)

A)  A		B)  B		C)  Same resistance.

Answer:  Since the two bulbs carry the SAME CURRENT, we use the formula P = I2R.  At the same current, the higher P has the higher resistance.    Bulb A has the higher resistance.

Compare this problem with 18-6.  In that problem, we compared bulbs with the same voltage.  Here we compare bulbs with the same current.

# Text boxes

1

I

E)  None of these will work

I

D

2

R = 10 Ω

V = 5 V

A

B

C

R

V = 5 V

hollow metal

insulator

metal

D)

-

+

C)

-

+

B)

-

+

A)

-

+

B

A

V

V

(A)

I

V

(D)

I

V

(C)

I

V

(B)

(E) None of these