QC-

The plates of a parallel plate capacitor are charged with equal and opposite charges +Q and –Q.  The plates are electrically insulated so their charges cannot change. The plates are pulled apart a little bit, so that the separation d of the plates is greater.

As the plates are pulled apart, the capacitance of the plates...

A) increased       B) decreased           C) stayed the same.

The energy stored in the capacitor...

A) increased       B) decreased           C) stayed the same.

(Hint: Did the person pulling the plates apart do positive work, negative work or no work?)

As the plates were pulled apart, the energy density (energy per volume) = u = (1/2)(oE2 ....

A) increased       B) decreased           C) stayed the same.

QC-

A parallel-plate capacitor with a dielectric between the plates is charged so that +Q resides on one plate, –Q on the other.  With the plates isolated and the charge Q constant, the dielectric is pulled out from between the plates. The energy stored in the capacitor ...

A) increased		B) decreased	C) stayed the same.

Hints: Did the electric field between the plates change? Was work done when the dielectric was removed?

# Text boxes

+Q

-Q

+Q

-Q