Faraday CT's

F- In which situation is the magnetic flux through the loop the smallest?

(A) Same flux in all three situations.

Answer: B  When the loop is edge-on to the field, the flux through the loop is zero.

F- A loop of wire is moving rapidly through a uniform magnetic field as shown.

True (A) or False(B): there is a non-zero emf induced in the loop.

Answer: False.  The magnetic flux through the loop is not changing (constant B-field, constant area A, constant angle between B-field and plane of loop), so the emf is zero.

A loop of wire is spinning rapidly about a stationary axis in uniform magnetic field as shown.

True(A) or False(B): there is a non-zero emf induced in the loop.

Answer: True.  There is a changing flux through the loop, since the angle between the B-field and the plane of the loop is changing.  A changing flux creates an emf.

F- The magnetic flux through a loop of wire is shown.  At which point is the emf induced in the loop a maximum?

Answer: The rate of change of flux (and hence the emf) is maximum at point B.

F- A loop of wire is sitting in a uniform, constant magnet field  as shown.  Suddenly, the loop is bent into a smaller area loop.  During the bending of the loop, the induced current in the loop is   A: zero		B: clockwise			C: counterclockwise

Answer: The flux is decreasing as the loop area decreases.  To fight the decrease, we want the induced B to add to the original B. By the right hand rule (version II) , a clockwise induced current will make an induced B into the page, adding to the original B. The answer is: Clockwise.

F- A bar  magnet is  positioned below a horizontal loop of wire with its North pole pointing toward the loop.  Then the magnet is pulled down, away from the loop.  As viewed from above, is the induced current in the loop clockwise or counterclockwise?

Answer: The B-field from a bar magnet points out of the North pole.  As seen from above, the field through the loop is out (toward the observer).  As the magnet is pulled away, the flux is decreasing.  To fight the decrease, the induced B-field should add to the original B-field, and also be out (toward the observer).   The induced current will be B), counterclockwise, in order to make an induced B-field out.

F- A square loop is rotating in a fixed, external magnetic field into the page.  At the instant shown, the loop is out of the plane of the page with left side of the loop above the page and coming out of the page, the right side is below the page going away.  The direction of the induced current is ...

Answer: At the moment shown, the flux through the loop is decreasing (since the amount of B-field "threading" the loop is decreasing.) To fight the decrease, the induced field should add to the original field.  The answer is B

F-  A loop of wire is near a long straight wire which is carrying a large current I, which is decreasing.  The loop and the straight wire are in the same plane and are positioned as shown.  The current induced in the loop is

A: counter-clockwise		B: clockwise		C: zero.

Answer: CW.  At the position of the loop, the B-field created by the long wire is into the page.  The flux is decreasing, so Lenz's law says the induced B-field should into the page, to add to the original flux and fight the decrease.  Right-hand-rule II says that to make B point into page, we need a clockwise induced current.

F-  Two loop of wires labeled A and B are placed near each other as shown.  A large current I in loop A is suddenly turned on.  This causes an induced current in loop B which causes

A: A net repulsive force - the two loops repel

B: A net attractive force - the two loops attract

C: whether the force is attractive or repulsive depends on whether the current in first loop is CW or CCW

D: No net force.

Answer: A) a repulsive force, the two loops repel.

Assume a CCW current I in Loop A. When the current I is turned on, there is an increasing B-field pointing out of the page in the middle of both loops A and B.  This increasing B-field outward induces a CW current in loop B so as to create an induced B-field into the page (fighting the increase in flux).   Now, you have to remember that anti-parallel currents repel; parallel currents attract.  The two currents are anti-parallel, so the loops repel.

If the current in loop A was the other way (CW), then everything would be reversed and the two currents would still be anti-parallel.

F-  A wire loop, moving right, enters a region where there is a constant, uniform magnetic field pointing into the page.

As the loop enters the B-field, the current induced in the loop is   A: CW	B: CCW

As the loop enters the B-field, the direction of the net force on the loop is ...

A: right (		B: left(		C: up (		D: (down

E: there is no net force

Answers:

Question 1: A) CCW.  As the loop enters the field, the flux increases. To fight the increasing flux, the induced B-field (out of the page) should be opposite the original B (into the page).  A CCW current will create an induced B out of the page.  This current is an example of an "eddy current".

Question 2: B) left.

Method I (the easy way ): The magnetic forces on eddy currents are always in the direction which opposes the motion.  (Otherwise you could make a perpetual motion machine).

Method II (harder way):  Work out all the directions.  As the loop enters the field, the flux thru the loop is increasing.  By Lenz's law, the induced current in the loop will be CCW [so that the induced B-field (out of the page) fights the change in flux].  There will be a magnetic force on the right side of the loop .  The direction of that force is to the left.

F-   The vertical wire shown is moving to the right in a uniform magnetic field which is into the page.  There is a current upward, meaning that there is a flow of electrons downward.  The fixed positive ions in the wire are moving to the right, along with the wire. The negative conduction electrons are moving to the right and down.  What is the direction of the net magnetic force on this segment of the wire?

A) Up 		B) Down 	 C) Left	D) Right	E) None of these

Answer: C) The net force on the wire is Left.  The force due to the rightward motion of the electrons is exactly cancelled by the force due to the rightward motion of the protons.  (Opposite-sign charges, so opposite-direction forces).  Only the downward component of the velocity of the electrons produces a force (leftward) which is unbalanced by the force on the protons.

F- An electric motor consists of a coil, free to turn on an axis, located in an magnetic field B created by an arrangement of permanent magnets.  With the current and field directions as shown, which way will the coil rotate?

A: CW

B: CCW

C: the coil won't rotate when at this particular orientation

Answer: The coil will turn counter-clockwise (B).

F-  A transformer is connected to a battery as shown. The voltage difference across the resistor R is

A)   V N2/N1

B) V N1/N2

C) V

D) zero.

E) not enough information to

answer.

Answer: It's a trick question!  Transformers only work with time-varying voltages: AC voltages.  The DC voltage V from the battery produces a DC current in the primary coil, but produces no voltage of any kind in the secondary coil.  Transformers work because of Faraday's Law: the changing flux produced by the AC current in the primary coil produces an emf in the secondary coil.  If the flux is not changing, there is no emf. The answer is Zero!!

F- The primary coil of a transformer is connected to a battery, a resistor, and a switch.  The secondary coil is connected to an ammeter.  When the switch is thrown closed, the ammeter shows..

A)   a zero current

B)  a non-zero current for a brief

instant

C)  a steady non-zero current.

Answer: B) There is a non-zero current briefly as the switch is closed but then there is no current after the switch has closed.  As the switch is closed, the current in the primary coil changes from zero to some non-zero value.  While the current is changing, there is a changing B-field and a changing flux which causes an emf in the secondary and a current flow in the secondary.

F-  A step-down transformer is attached to an AC voltage source and a resistor as shown.  How does the current in the resistor I R compare to the current in the drawn from the AC source Iinput?  (With AC circuits, we always use rms values of I and V.)

A) I R  >  I_in

B) I R  <  I_in

C) I R  =  I_in

D) Depends on the value of Iin

Answer: When the voltage is stepped down, the current must be stepped up (since powerin = powerout so P = IV is constant)

F-  An electrical engineer at a power plant wants to reduce the energy wasted during power transmission from the plant to the city.   The power output Po=IV of the plant is fixed at 100MW.  The engineer decides to double output voltage V.   By what factor does the power lost in the cable (Plost = I2 Rcable) decrease?  (Hint: if P=IV is fixed, when V goes up, I goes down.)

A) No decrease

B) factor of 2 decrease

C) factor of 4 decrease

D) factor of 8 decrease

Answer: The power lost in the cable decreases by a factor of 4.  If V doubles, then I decreases by a factor of 2 (since P = IV is constant).  If I decreases by a factor of 2, then I2 decreases by a factor of 4.

F-  A long, straight wire carrying an increasing current I passes along a diameter of a wire loop.  The straight wire and the loop are in the same plane but are not in electrical contact.

The induced current in the loop is:

A)  zero.

B)  counter-clockwise

C)  clockwise.

Answer: A), zero.  The total flux in the loop (due to the straight wire) is zero at all times.  The B-field on the right half of the loop is into the page; the B-field on the left half is out of the page.  The definition of flux is , where ( is the angle between the normal to the loop and the B-field.  For half of the loop, the angle ( = 0, cos( =1; for the other half of the loop, ( = 180, cos( = -1.  The two halves have opposite sign flux and they cancel.  Since the flux is always zero (which is a constant), the time rate of change of flux is zero, so no emf, no induced current.

F-  A rectangular loop is placed in a uniform magnetic field with the plane of the loop perpendicular to the direction fo the field.  If a current is made to flow through the loop in the sense shown by the arrows, the field exerts on the loop...

A) a net force only

B) a net torque only

C) a net force and a net torque

D) neither a net torque nor a net force.

Answer: D), No net torque and no net force.  Using the right hand rule for each side of the square loop, the force on each side is away from the center of the loop.  The net force and net torque are both zero.

# Text boxes

loop

axis of rotation

area A

tilted 60°

C) Neither

area A

face-on

B

axis

C

B

A: clockwise

B: counter-clockwise

N

S

eyeball

B(in)

A

B

B

B

I

B

A

area 2A

edge-on

(D)

(C)

(B)

iron

core

B

A

A

D

motion of

conduction electrons in wire

flux (

motion of wire and

of fixed positive ions

time

electron current

conventional

current I

B(in) uniform

V(AC)

I increasing

I

IR

I_in

constant

uniform

B-field

B(in)

B(in)

I to the right, but decreasing.

V

R

N1

N2

R

iron core

V

Rcity

(adjusted to keep

P=IV constant.)

I

Rcable

loop

No electrical contact between

loop and straight wire.

B