Concept Tests -- Final Review

CTF-

A square with edge length L is made larger and larger...

As the square grows, the ratio ..

A) increases		B) decreases	C) remains constant.

CTF-

Which of the following is a solution for x?

A) x = 1– d  			B) x = d2  + 1

C) x = 1 + 2d + d2		D) x = 0 		E) None

CTF-

A box with mass M and charge +Q is pushed along a rough surface at constant velocity by a uniform horizontal electric field of magnitude E.  The coefficient of kinetic friction between the box and the floor is .   What is the net force on the box?

A) Q E		B) g		C) zero

D) Q E – M g + FN – Mg .

(FN is the magnitude of the normal force on the box.)

CTF-

Charges +Q and –Q  and a third unknown charge are all a distance R from point x.  What value of the unknown charge will produce a net electric field Etot = 0 at point x?

A) +Q

B) 0

C) –2Q

D) –Q

E) There is no value which will make Etot = 0 at point x.

CTF- Points A and B are distances r and 3r respectively from a point charge q.  What is the voltage difference between points A and B?

A)		B) 		D)  		C) None

CTF-

Consider a point in empty space near several point charges, which might be positive, negative, or both.  Consider the following statements.

I. The E-field can be zero while the voltage is non-zero.

II. The voltage can be zero while the E-field is non-zero.

Which of these statements can be true?

A) both can be true		B) neither can be true

C) only I can be true		D) only II can by true

CTF-

A capacitor has a voltage V across its plates.  An electron, initially at rest, is released from a point very close to the negative plate of a capacitor and it accelerates toward the positive plate.   The electron has charge – e and mass m.  There is no gravity in this problem, and you may assume that the motion of the electron is non-relativistic.  What is the final kinetic energy of the electron just before it collides with the positive plate?

A)

B) 2eV

C) (1/2)mV2

D) eV

CTF- A resistor of resistance R is plugged into a 120VAC wall socket.  The graph below is either resistance R, voltage V across, current I in, or power P dissipated in the resistor vs. time.

What could the graph be?

A) V only		B) I only		C) V or I only

D) R or P only 	E) V, I, or P

CTF-

Consider the circuit shown, with the switch initially open. When the switch is closed, the current I1 through resistor R1

A) increases,

B) decreases,

C) stays the same.

CTF-

When the switch is closed, the current from the battery Ibat

A) increases, 	B) decreases, 		C) stays the same.

CTF-

When a particular resistor is plugged into a standard AC outlet, the fuse blows and all the lights go out.  If we want to repeat this dangerous experiment, and not have the fuse blow,  we need a resistor that is

A) larger		B) smaller

C) Same R, but larger power rating

CTF-.

A charge q is released from rest at point in empty space were there may be E- and/or B-fields.  There are no forces on the charge except for the forces due to the E and/or B-fields (no gravity, etc.).  The charge is observed for a short while and is seen to move along a curved path ("curved" means "not straight", but not necessarily circular.)

Consider the following possibilities

I. There is only an E-field present and no B-field.

II. There is only a B-field present and no E-field.

III. There is both an E-field and a B-field present.

Which possibilities could account for the observed motion?

A) all three 		B) I and III only

C) II and III		D) III only

CTF-

At time to, a particle with charge q has instantaneous velocity v as shown and is moving in a uniform magnetic field B that is parallel to the x-axis.

A) True 	or   B) False:

As time increases, the x-component of the velocity vx remains constant.

CTF-

A horizontal loop of wire is in a vertical magnetic field.  The magnetic field varies linearly with time, changing smoothly from pointing upward to pointing downward, as shown. (The B-field gradually gets smaller, goes to zero, then grows in the other direction.)

At the moment when the magnetic field in the loop is zero, is there an induced current in the loop?

B) Yes	C) No

CTF-

What is the direction of the induced current?

B) Clockwise (as seen from above)	C) Counterclockwise

CTF-

Two different radio towers, labeled I and II, both emit the same power Po.  Tower I emits isotropically (uniformly in all directions).  Tower II emits only to the East, uniformly over a hemisphere.  Consider a receiver at a distance R from both towers.   (The towers broadcast at different frequencies so there is no constructive or destructive interference at the receiver; both signals are received independently.)

Which signal will be stronger?

A) Signal I		B) Signal II	C) Both are equal strength.

CTF-

Is the image formed by the lens in your eye real or virtual?

A) real 	B) virtual

CTF-

An object is placed nearer to a converging lens than the focal length f of the lens.  The image formed is :

A) Real and the image is further from the lens than 2f

B) Real and image is between f and 2f distance from the lens

C) Virtual and closer to the lens than the object

D) Virtual and further from the lens than the object

CTF-  A double slit interference pattern is seen on a screen

The path difference (p.d.) for a given point on the screen is the quantity [(distance to slit 1) - (distance to slit 2)].

What is the path difference at point A?

A) 5(		B) 3(		C) 2(	 D) 1.5(

E) None of these

Don't forget to review Modern Physics and Special Relativity!

# Text boxes

B

V

x

v=constant

-Q

R

E

M, Q

f

II

object

receiver

f

q

D

q

R

?

I

+Q

?

C

R

V

wavelength

λ

A

B

µ

r

2r

q

A

B

time

R1

R2

Ibat

I1

y

x

v

A

screen

fringes

d

slit 1

slit 2