Concept Tests -- Final Review

CTF-

A square with edge length L is made larger and larger...

As the square grows, the ratio ..

B) increases		C) decreases		D) remains constant.

Answer:  The ratio is 4L/(L2) = 4/L.  The ratio decreases

CTF-

Which of the following is a solution for x?

A) x = 1– d  			B) x = d2  + 1

C) x = 1 + 2d + d2		D) x = 0 		E) None

Answer: A)

CTF-

A box with mass M and charge +Q is pushed along a rough surface at constant velocity by a uniform horizontal electric field of magnitude E.  The coefficient of kinetic friction between the box and the floor is .

What is the net force on the box?

B) QE		C) g	D) zero	E) QE - Mg + FN -  Mg .

(FN is the magnitude of the normal force on the box.)

Answer: D), Acceleration is zero, so the net force must be zero.  All the forces cancel.

CTF-

Charges +Q and –Q and a third unknown charge are all a distance R from point x.  What value of the unknown charge will produce a net electric field Etot = 0 at point x?

A) +Q

B) 0

C) –2Q

D) –Q

E) There is no value which will make Etot = 0 at point x.

Answer: E)

CTF-

Points A and B are distances r and 3r respectively from a point charge q.  What is the voltage difference between points A and B?

B)		C) 	D)  		E) None of these.

Answer:  Voltage due to a point charge is kq/r.  The voltage difference between points A and B is (kq/r - kq/(3r)) = 2kq/3r.

CTF-

Consider a point in empty space near several charges, which might be positive, negative, or both.  Consider the following statements.

I. The E-field can be zero while the voltage is non-zero.

II. The voltage can be zero while the E-field is non-zero.

Which of these statements can be true?

B) both can be true		C) neither can be true

D) only I can be true	E) only II can by true

Answer:  Both can be true.

CTF-

A capacitor has a voltage V across its plates.  An electron, initially at rest, is released from a point very close to the negative plate of a capacitor and it accelerates toward the positive plate.   The electron has charge -e and mass m.  There is no gravity in this problem, and you may assume that the motion of the electron is non-relativistic.  What is the final kinetic energy of the electron just before it collides with the positive plate?

B) 		C) 2eV

D) (1/2)mV2			E) eV

Answer:   |(KE| = |(PE| = |q(V| = eV

CTF-

A resistor is plugged into a 120VAC wall socket.  The graph below is either voltage V across, current I in, or power P dissipated in the resistor vs. time.

What could the graph be?

B) V only		C) I only		D) V or I only

E) V, I, or P

Answer: The graph could be V or I only.  Power is always positive.

CTF-

Consider the circuit shown, with the switch initially open. When the switch is closed, the current I1 through resistor R1

B) increases,

C) decreases,

D) stays the same.

Answer: stays the same.  I1 = V/R1 regardless of whether or not the switch is closed.  What does change is the battery voltage.

CTF-

When the switch is closed, the current from the battery Ibat

B) increases, 	C) decreases, 		D) stays the same.

Answer: increases.  With the switch closed, the battery must supply current to R2 as well as to R1.

CTF-

When a resistor is plugged into a standard AC outlet, the fuse blows and all the lights go out.  If we want to repeat this dangerous experiment, and not have the fuse blow,  we need a resistor that is

B) larger		C) smaller

D) Same R, but larger power rating

Answer: larger.  At constant voltage (here V = 120 VAC), the power is P = V2/R.  Larger resistance draws less power.

CTF-

A charge q is released from rest at point in empty space were there may be E- and/or B-fields.  There are no forces on the charge except for the forces due to the E and/or B-fields (no gravity, etc.).  The charge is observed for a short while and is seen to move along a curved path.

Consider the following possibilities

I. There is only an E-field present and no B-field.

II. There is only a B-field present and no E-field.

III. There is both an E-field and a B-field present.

Which possibilities could account for the observed motion?

B) all three 		C) I and III only	D) II and III		E) III only

Answer: I and III only.  A curved E-field and no B-field could produce the motion shown.

CTF-

At time to, a particle with charge q has instantaneous velocity as shown and is moving in a uniform magnetic field .

B) True

C) False

As time increases, the x-component of the velocity vx remains constant.

Answer: True.  The force exerted by the magnetic field is into the page (right-hand rule).  This force has no x-component.  Since there is no x-component of the force, the x-component of the acceleration must be zero, and the x-component of the velocity must be zero.

CTF-

A horizontal loop of wire is in a vertical magnetic field.  The magnetic field varies smoothly from pointing upward to pointing downward, as shown. (The B-field gradually gets smaller, goes to zero, then grows in the other direction.)

At the moment when the magnetic field in the loop is zero, is there an induced current in the loop?

B) Yes		C) No

Answer:  Yes.  Even though the B-field is instantaneously zero, it is still in the process of changing (from up to down). So the time-rate of change of B is non-zero, and by Faraday's Law, there must be an emf and an induced current.

CTF-

What is the direction of the induced current?

B) Clockwise (as seen from above)	C) Counterclockwise

Answer: Counterclockwise.  Lenz's Law.

CTF-

An radio tower is emitting a single-wavelength (monochromatic) EM wave in all directions (isotropically).  A technician measures the electric field amplitude E at 100 meters from the tower and again at 400m from the tower.  What is the ratio E100/E400?

(Hint: Intensity is proportional to the square of the amplitude: I ( E2)

B) 2		C) 4		D) 16	 	E) 162 = 256

Answer: 4  The intensity is 16 times greater at 100 m than at 400 m, but the E-field is only 4 time greater.

CTF-

Two different radio towers, labeled I and II, both emit the same power Po.  Tower I emits isotropically (uniformly in all directions).  Tower II emits only to the East, uniformly over a hemisphere.  Consider a receiver at a distance R from both towers.   (The towers broadcast at different frequencies so there is no constructive or destructive interference at the receiver; both signals are received independently.)

Which signal will be stronger?

A) Signal I		B) Signal II	C) Both are equal strength.

XXX

Answer: C), Both are the equal strength.  The receiver only absorbs the signals that touch it.  The signals that are pointed away from the receiver make no contribution to the signal strength.

CTF-

Is the image formed by the lens in your eye real or virtual?

B) real 	C) virtual

XXX

Answer: B) real.

CTF-

An object is placed nearer to a converging lens than the focal length f of the lens.  The image formed is :

A) Real and the image is further from the lens than 2f

B) Real and image is between f and 2f distance from the lens

C) Virtual and closer to the lens than the object

D) Virtual and further from the lens than the object

Answer: D), Virtual and further from the lens than the object.

CTF-

A double slit interference pattern is seen on a screen

The path difference (p.d.) for a given point on the screen is the quantity [(distance to slit 1) - (distance to slit 2)].

What is the path difference at point A?

B) 5(		C) 3(		D) 2(

E) None of these

Answer: None of these.  The first min occurs when the path difference is (/2.

CTF-

The rest mass energy of an electron is  .    An electron is accelerated from rest across a voltage V.  At what voltage V is the final kinetic energy of the electron equal to its rest mass energy?

B) V=0.511 MV	C) 1.022 MV		D) 1.533 MV

E) None of these.

Answer: V=0.511 MV

# Text boxes

x

+Q

A

v=constant

E

2r

I1

V

time

B

R

-Q

?

v

V

q

q

µ

I

M, Q

?

x

r

R1

II

R

R

R2

Ibat

y

q

B

E measured at 100m

E measured at 400m

receiver

f

object

A

B

C

D

f

|di|

|do|

optic axis

image

(virtual!)

object

slit 2

slit 1

wavelength

λ

A

screen

fringes

d