Magnetism Concept Tests.

CTM-  Pick the answer which is most nearly correct.

Magnetic fields are caused by...

A) stationary electric charges.

B) magnetic monopoles.

C) moving charges (currents)

D) neutrinos

E) None of these is correct.

CTM-

A negative particle and a positive particle are moving with given velocities in a constant, uniform magnetic field B, as shown.  The direction of the B-field is to the right.  The (+) particle is moving directly left; the (–) particle is moving directly up.

The force on the negative particle due to the B-field is

A: in		B: out		C: zero		D: right		E: left

The force on the positive particle due to the B-field is

A: in		B: out		C: zero		D: right		E: left

CTM-

A positive particle is released from rest in a region of space where there  is constant, uniform, electric field E, and a constant, uniform magnetic field B.  The electric field points up and the magnetic field points out of the page in the diagram below. Which path will the positive particle follow?

The work done by the magnetic field on the particle is..

A) positive		B) negative 	C) Zero.

CTM-

A proton (charge q = +e), moving to the right with an initial speed v, passes into a region where there is a vertical electric field pointing down and a horizontal magnetic field pointing into the page.  Is it possible that the forces from the E- and B-fields cancel and the proton moves straight through undeflected.  (Ignore gravity in this problem.)

A) Yes, the forces can cancel and the particle moves straight through

B) No, the forces cannot perfectly cancel; the particle path will be bent.

The E- and B-fields of the velocity selector are adjusted so that protons with a certain speed v pass through undeflected.  Now electrons with the same speed are shot into the velocity selector (with same E- and B-fields as before).  Do the electrons also pass through undeflected?

A) Yes, the electrons go straight through

B) No, the electrons are bent

CTM-

A particle with unknown charge (but non-zero) q and moving left with speed v enters a regions where there is a uniform electric field down and a uniform magnetic field out of the page.   The particle is observed to go in a straight line.  The charge of the particle must be  ...

A: positive		B: negative		C: impossible to determine.

Suppose the particle is a proton. If the speed of the proton is increased, it will

A: still undergo no deflection

B: deflect out of the plane of the page

C: stay in the plane of the page and deflect upward

D: stay in the plane of the page and deflect downward

CTM-

A square loop of wire carrying current I is in a uniform magnetic field B.  The loop is perpendicular to B (B out of the page).  What is the direction of the net force on the wire?

A: out of the page

B: into the page

C: (

D: (

E: None of these

The same loop is now in a non-uniform field.   The field grows stronger near the bottom of the page.  The direction of the net force is ...

CTM-

A magnetic compass is placed at the points A, B, and C near an electric circuit which has the following twisty shape:

The deflection of the compass needle is a measure of the strength of the magnetic field.  The relative deflection of the needle n order from biggest to smallest deflection is..

A) ABC		B)  CAB		C)  BCA

D)  ACB		E)  None of these.

CTM-

4 parallel wires each carry a current I.  3 of the wires carry current out the page, 1 carries current into the page, as shown.  What is the direction of the B-field at the center of the square?

CTM-

A rectangular loop of wire is carrying a current i in the clockwise direction and is near a long straight wire carrying a current I, as shown.  What is the direction of the net force on the rectangular loop, due to the B-field from the long, straight wire.

CTM-

A positively-charged particle with an initial speed vo is moving in a plane perpendicular to a uniform magnetic field (B into the page).  There is a tenuous gas throughout the region which causes viscous drag and slows the particle over time.  The path of the particle is

A: a spiral inward	B: a spiral outward 	C: something else

If the time for the particle  to complete the first revolution (once around) is 1 second, the time for the first 5 revolutions is

A: > 5 s		B: < 5 s		C: 5 s

CTM-

A square loop of wire carrying a current I, is in a constant uniform magnetic field B.  The magnetic field is perpendicular to the plane of the loop. The loop can rotate freely about the axis.

The loop tends to rotate so that the near edge moves..

A) to the right

B) to the left

C) The net torque on the loop is zero, so it does not tend to move.

CTM-

A permanent bar magnet is broken in half.  The two pieces are interchanged, keeping their orientations fixed, as shown below.  Do the pieces attract or repel?

A)  Attract

B)  Repel

C) No force at all.

CTM-

A row of positive charges sites stationary on the ground.  A person with a gauss-meter(which measures the magnetic field) is running to the right along the row of charges, at the same height as the charges and in front of them (in the diagram below).  What is the direction of the B-field which the observer measures?

CTM-

A loop of wire is brought near a long straight wire carrying a current I.  The direction of the current induced in the loop is..

A: Clockwise			B: Counter-clockwise

C: Not enough information to tell.

# Text boxes

A

E) it move out of the plane of the page

B

E

A: Zero

2

B

E) None of these

I

B(out)

B

C

D) it will remain stationary

A, B, and C in plane of diagram

C)

I

D

B

C

A

B stronger

B weaker

E: net force is zero

I

B (out)

???

+

E

B

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

+ + + + + + + + + + + + + + + + + + + + + + +

v

B

E

B)

A)

D)

C)

B)

Hint:

y

x

(out)

(out)

(out)

(in)

E) Net force is zero

C)

B)

D)

A)

i

I

Near edge

axis

Far

edge

B

2

1

1

C:

(forward

direction)

E: (down)

D: (backward

direction)

B: (up)