CT19-1.

Vote TRUE(D) if both statements below are always true.   Otherwise, vote FALSE(E).

TRUE (D) or FALSE(E) ?

- For resistors in series, the current through each resistor is the same.

- For resistors in parallel, the voltage across each resistor is the same.

NOTE! Vote "D" or "E",  NOT A or B.

ANSWER: Both statements are TRUE.

Ch19-2.

A 1( resistor is placed in parallel with a 10,000 ( resistor as shown.

The total, equivalent resistance of these two resistor in parallel is closest to...

A)  a little less than 1(		B)  a little more than 1(.

C)  5000 (				D)  a little less than 10000(

E)  a little more than 10000(

Answer: a little less than 1(.  You could use the formula ,   .  Or, just think:   1( is a very low resistance compared to 10000(, so almost all the current will flow through the 1( resistor, the circuit will behave almost as if the 10000( resistor is not present, and the equivalent resistance is close to 1(.  The question is:  is the equivalent resistance a little less or a little greater than 1(.  Adding the 10000( resistor in parallel provides another current path of the flow of charge.  More flow means lower resistance.

Q19-3

The circuit below consists of a battery attached to two resistors in series.  Resistor R1 is variable.

When R1 is decreased, the voltage V2 across R2 ...

A)  increases		B)  decreases		C)  stays the same.

Answer: increases.  This is easiest to see if you let R1 go all the way to zero!    Kirchhoff's 2nd Law says that the battery voltage V=V1+V2.  The voltage drop is split between resistors 1 and 2.  So V2 is smaller than the battery voltage V.  But if R1=0, then the full battery voltage V is across R2.  V2 increased as R1 goes down.

Q19-5.

The four light bulbs shown are identical.  Which circuit puts out more light? (Hint: more power = more light).

(A)							(B)

(C) They both put out the same amount of light.

Answer: The total equivalent resistance which the battery in the (A) circuit sees is R/2 (two resistors, each of resistance R in parallel) The total equivalent resistance which the battery in the (B) circuit sees is 2R (two resistors in series).  The total power coming from the battery is

.    Smaller Rtot (with fixed V) results in a larger power P.   So (A) puts 4 times as much power; it puts out more light.

Q19-6.

In the circuit below, what happens to the brightness of bulb 1,  when bulb 2 burns out?   (When a bulb burns out, its resistance becomes infinite.)

A) Bulb 1 gets brighter

B) Bulb 1 gets dimmer.

C)  It's brightness remains the same.

(Hint: What happens to the current from the battery when bulb 2 burns out.)

Answer: B). When bulb 2 burns outs, the filament inside breaks and R2 becomes infinitely large.  The total equivalent resistance which the battery sees increases (since bulb 2 is gone, there are fewer paths for the current flow, so less flow, more total resistance.)  Since the battery sees a larger Rtot, the current from the battery Itot = V/Rtot is reduced.  Less current from the battery means less current through bulb 1, less light.  Bulb 1 gets dimmer.

# Text boxes

V

V = 12V

10,000 Ω

1 Ω

I

I2

V2

I1

V1

R1

R2

2

3

1

V = 12V

V = 12V