Chapter 20 Concept Tests.

Reading Quiz:

Pick the answer which is most nearly correct.

Magnetic fields are caused by...

A) stationary electric charges.

B) magnetic monopoles.

C) moving charges (currents) .

D) particles with both mass and charge.

E) None of these is correct.

Answer: moving charges (currents) .

Q20-1

A negative particle and a positive particle are moving with certain velocities in a constant, uniform magnetic field , as shown.  The direction of the B-field is to the right.  The (+) particle is moving directly left; the (–) particle is moving directly up.

The forces on the two particles are (in = into page,  out = out of page).

A) 	+ in		– zero

B)	+ out		– in

C) 	+ zero		– out

D)	+ zero		– in

E) 	None of these.

Answer: The (+) particle is moving anti-parallel to the B-field.  The angle ( is 180 and the force is FB=qvB sin( = 0.

The (-) particle is moving at right angles to the field.  By the right-hand rule, the direction of the force is out of the page.

Q20-2

A positive particle is released from rest in a region of space where there  is constant, uniform, electric field , and a constant, uniform magnetic field .  The electric field points up and the magnetic field points out of the page in the diagram below. Which path will the positive particle follow?

The work done by the magnetic field on the particle is..

A) positive	B) negative 	C) Zero.

Answer: The (+) particle will feel a force FE = qE due to the E-field along the direction of the E-field.  As it starts moving along the E-field direction, it will acquire a velocity, and it will start to feel a force FB=qvB, due to the B-field.  The direction of the force is to the right, by the right-hand-rule.  So the particle moves up and to the right.

Q20-3

A magnetic compass is placed at the points A, B, and C near an electric circuit which has the following twisty shape:

The deflection of the compass needle is a measure of the strength of the magnetic field.  The relative deflection of the needle n order from biggest to smallest deflection is..

A) ABC		B)  CAB		C)  BCA

D)  ACB		E)  None of these.

Answer: The correct order is CAB.  Big currents make big magnetic fields.  Near C there are two currents in the same direction which are effectively one big current.  Near B, there are two equal currents going in opposite directions, which if they were right on top of each other would give a net current of zero.  Point A is the middle case.

Q20-4

A rectangular loop of wire is carrying a current i in the clockwise direction and is near a long straight wire carrying a current I, as shown.  What is the direction of the net force on the rectangular loop, due to the B-field from the long, straight wire.

Answer: The direction of the net force is up.  The B-field created by the long straight wire is into the page at the location of the loop (by Right Hand Rule II).  The upper portion of the loop feels an upward force and the bottom portion of the loop feels a downward force (by the Right hand rule).  But the field is larger at the top potion of the loop because the B-field is larger closer to the straight wire.  So the upward force on the upper wire in the loop is larger than the downward force on the lower wire.

Another way to see the answer:  Parallel currents attract and anti-parallel currents repel.  So the upper portion of the loop feels an upward force and the bottom portion of the loop feels a downward force.  But the upper portion is closer to the straight wire, so there is a bigger field, a bigger force.

Q20-5

A square loop of wire carrying a current I, is in a constant uniform magnetic field B.  The magnetic field is perpendicular to the plane of the loop. The loop can rotate freely about the axis.

The loop tends to rotate so that the near edge moves..

A) to the right

B)  to the left

C) The net torque on the loop is zero, so it does not tend to move.

Answer: Since from above looking down along the axis of rotaion,  the situation is as shown below.  The direction of the forces are from the Right hand rule.  Both edges feel a force inward toward the axis of rotation. The net torque is zero; there is no tendency to rotate. The net torque is zero.

Q20-6

4 parallel wires each carry a current I.  3 of the wires carry current out the page, 1 carries current into the page, as shown.  What is the direction of the B-field at the center of the square?

Answer: Each of the four currents (labeled 1, 2, 3, 4 below) creates a B-field at the cent of the square.  The net B-field is the vector sum of these 4 fields and it points to the upper right.

Q20-7

A permanent bar magnet is broken in half.  The two pieces are interchanged, keeping their orientations fixed, as shown below.  Do the pieces attract or repel?

A)  Attract

B)  Repel

C) No force at all.

Answer: They attract. The bar magnet can be thought of as a solenoid of current. Parallel currents attract. When the magnet is broken and rearranged, the currents on the ends are parallel so there is an attraction.

(In the diagram, below we choose the right end to be North.  If we had chosen the right end to be South, all the currents would be reversed, but the end currents would still be parallel.

Q20-8

A proton (charge q = +e), moving to the right with an initial speed v, passes into a region where there is a vertical electric field pointing down and a horizontal magnetic field pointing into the page.  Is it possible that the forces from the E- and B-fields cancel and the proton moves straight through undeflected.  (Ignore gravity in this problem.)

B) Yes, the forces can cancel and the particle moves straight through

C) No, the forces cannot perfectly cancel; the particle path will be bent.

The E- and B-fields of the velocity selector are adjusted so that protons with a certain speed v pass through undeflected.  Now electrons with the same speed are shot into the velocity selector (with same E- and B-fields as before).  Do the electrons also pass through undeflected?

B) Yes, the electrons go straight through

C) No, the electrons are bent

Answer: Question 1. Yes, the forces can cancel and the particle moves straight through.  The electric field force is down and has magnitude eE (since FE = qE, and q = +e).  The magnetic field force is up (by the right-hand rule) and has magnitude evB.  The two forces exactly cancel when eE = evB, or v = E/B.

Question 2. Yes, the electrons go straight through.  Electrons have the same size charge as the proton, just opposite sign.  So both the electric force and the magnetic forces have the same magnitude as before, only the directions are switched.  The forces still cancel.

# Text boxes

D) it will remain stationary

C)

I

E

???

F

North

(A, B, and C are in the plane of the diagram)

E) Net force is zero

E) it will move out of the plane of the diagram

B (out)

B

C)

A)

B)

B)

A)

C)

B)

D)

A)

i

I

Near edge

axis

Far

edge

B

F

B

B

I(in)

I(out)

E) None of these

D)

C)

B)

Hint:

y

x

(out)

(out)

(out)

(in)

y

x

3(out)

1(out)

2(out)

4(in)

1

4

3

2

2

2

1

1

North

North

North

North

South

South

South

South

South

2

2

1

1

+

E

B

- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

+ + + + + + + + + + + + + + + + + + + + + + +

FB=evB

FB=evB

proton

electron

+

FE=eE

FE=eE