## Slide 1
B6
An ideal ammeter should have
Zero resistance
Infinite resistance

## Slide 2
B4
Is it possible to measure the current generated by the power supply using the scope?
No, it only measures voltage
Yes, just turn the knob on the scope from “V” to “I”
Yes, put a resistor in the circuit and measure the voltage across it.

## Slide 3
B8
An ideal voltmeter should have
Zero resistance
Infinite resistance

## Slide 4
B3
What is Zeq?
A)
B)
C)
D)
E)
R
L

## Slide 5
B2
What is Vout/Vin?
A)
B)
C)
D)
E)
Vin
Vout
R2
R1

## Slide 6
C1
What is VTh?
V
V R2/(R1+R2)
V R1/(R1+R2)
V(R1+R2)
0
V
R1
R2

## Slide 7
C3
What is RTh?
R1
R2
R1+R2
R1 R2/(R1+R2)
R2/(R1+R2)
V
R1
R2

## Slide 8
C0
What is Vout?
V
V R/(R+jωL)
V jωL/(R+jωL)
V (R+jωL)
0

## Slide 9
C2
What is ZTh?
0
(R/jωL)/(R+jωL)
R
1/jωL
jωLR/(R+jωL)
V
R
L

## Slide 10
C5
0 V
2.5 V
3.3 V
5 V
7.5 V
10V
1MW
1 MW
The input impedance of most scopes is 1 MW. What voltage does the scope measure across the lower 1 MW resistor?